## Slide 1: Automating LCA from CAD models for sustainable design feedback
MDENet Annual Symposium 2023
Department of Engineering
Dr Francesco Ciriello
06/12/2023
Natural, Mathematical & Physical Sciences
Department of Engineering
Antoine El Adib
This work was supported by

## Slide 2: Learning Outcomes
Review the educational requirements for introducing LCA-driven decision-making systems in engineering design modules
Explain how physical properties are stored and retrieved with the hierarchy of CAD project
Critique the scope, assumptions, inventory and performance indicators in an LCA analysis
Review progress on the seedcorn project and next steps

## Slide 3: A Decision-Support System for Sustainable Design
How can we meaningfully connect sustainability assessment to design activities?
Notes: A sample demo output of what we intend to develop

## Slide 4: Principles of an Automated Feedback System
Inputs
Parameters, Options, Methods, Variants, Decisions
Outputs
Visualisations, Data Analytics, Severity Levels, Text Reporting, Error & Warning Messages
Multi-user interaction
Clicks, Sensors
Artifact Evaluation
Design query
Design analysis
Feedback generation
Criteria & guidelines
Customisation based on ILOs
Assessment & Correction
Iteration support
Documentation & Resources
Orientation
Artifact
requirements, model, simulation, test, presentation, report, discussion
Comparative analysis
Feedback history and tracking (footprints)
Design implementation
Suggestions, Reflection Prompts & Feedback Rationale

## Slide 5: Our progress so far
Inputs
Variants
Outputs
Visualisations & Data Analytics
Single-user interaction
Clicks, Sensors
Artifact Evaluation
Extract Performance & Sustainability PIs
Design query
Design analysis
Feedback generation
Assessment & Correction
Iteration support
Artifact
CAD model
Comparative analysis
Design implementation

## Slide 6: Agenda
Sustainable Design Pedagogy
CAD Modelling requirements
LCA Modelling requirements
Visualisation & Decision Making

## Slide 7: KCL Engineering Design
Model-driven development with build & test to
  motivate learning
  validate experiments, data analysis and simulation
  develop practical skills
Pedagogical tensions between
  Exemplarity vs. Authenticity
  Scaffolding vs. Ambiguity, Creativity & Judgment

## Slide 8: Technical communication in engineering design
Technical drawings
Assembly diagrams
Part diagrams
Fabrication diagrams
Requirements & Specifications
Bill of Materials
Parameter / Technical Specification Sheets
Analysis & Test reporting
Parameter | Value
mass | 1.2 kg
cost | £42.34
max speed | 0.1 m/s
min turn radius | 0.3 m
… | …

## Slide 9: What are CAD models?
geometry & transformations
assemblies & components
materials
physical properties

## Slide 10: Our Virtual Component Library

## Slide 11: Our Virtual Component Library
couplings, shafts & sockets
gears
motors
stock materials
electrical
propellers
How can we automatically retrieve information from
  our virtual library?
  a new design assembled from its components?

## Slide 12: GraphQL Schema of a Fusion 360 CAD Model
https://mfgdatamodel-explorer.autodesk.io/voyager

## Slide 13: GraphQL Schema of a Fusion 360 CAD Model
https://mfgdatamodel-explorer.autodesk.io/voyager

## Slide 14: GraphQL Query
.json file with material and mass data from a Fusion project / folder / assembly

## Slide 15: Power Query Import

## Slide 16: Dig into a model hierarchy
query getAllModelOccurrences($componentVersionId: String!) {
componentVersion(componentVersionId: $componentVersionId) {
id
name
allModelOccurrences {
results {
parentComponentVersion {
id
name
}
componentVersion {
id
name
materialName
physicalProperties {
mass {
value
}
}
allModelOccurrences {
results {
parentComponentVersion {
id
name
}
componentVersion {
id
name
materialName
physicalProperties {
mass {
value
}
}
}
}
}
}
}
}
}
}
Model
Level 1 Components
Aggregate Level 1 Value
Level 1 Parent
Level 2 Components
Aggregate Level 2 Value
Level 2 Parent
Nominal Material
Nominal Material

## Slide 17: Life Cycle Assessments of Prototypes
Cut & print materials
Plywood
Acrylic
PLA
PETG
Styrofoam (polystyrene)
Electromechanical
Arduino Nano 33 IoT
Li-Ion & NiMh batteries
Servomotors
Brushed DC motors
Mechanical
Socket Couplings
Fasteners
Universal Joints
Propellers
How can we enrich this dataset to improve our decision making in design?

## Slide 18: Modelling requirements for LCA from CAD
Inputs
Material properties
  Name / ID
  Density, g/cm3
  Carbon contribution per unit / volume, g or g/cm3
Supplier properties
  Manufacturer ID
  Cost per volume / unit ($)
  Carbon contribution per unit / volume, g or g/cm3
Component properties
  Volume, cm3
  Stock Volume from bounding box in cm3
Outputs
Cost per component, £
Mass, g
CO2 potential impact per component, gCO2eq
Alternatives
CO2 potential savings per component, gCO2eq
Other impacts

## Slide 19: Planetary Boundaries & Sustainability KPIs
Credit: Stockholm Resilience Centre (2023)
Global Warming Potential – 100 years (GWP-100a)
measured in kgCO2eq
Acidification Potential
measured in kgSO2eq
Ecotoxicity
measured in g1, 4DCBeq
Water use
measured in m3
Energy use
measured in MJ

## Slide 20: Life Cycle Impact Assessment (LCIA) Fundamentals
Credit: ILCD (2010)
Life Cycle Assessments address the assessment of the environmental aspects of a product or service in its entire life cycle stages (ISO 14040)
Goal definition: What do we want to achieve?
Scope definition: What are our system boundaries?
Raw material extraction
Energy production
By-Products
Emissions
to environment
Plywood Sheet
Use Phase
Manufacturing Process
Cradle to gate
Transport
Cradle to grave
End Of Life

## Slide 21: Constructing an OpenLCA-derived database for the design modules
In Eco Invent Markets are default activities with data from known suppliers/location
Process translated from our system boundaries to EcoInvent
A process diagram for plywood production in Open LCA

## Slide 22: Constructing an OpenLCA-derived database for the design modules
Part
ID
Name
Supplier
Material
Mass
Cost
Impact

## Slide 23: Power Query Merge

## Slide 24
Inputs | Model | Outputs
 | Warnings: These components don’t have data. | Automated Design Feedback
modelName
Level 1
Level 2
Level 3
Component Tree Diagram
Fusion Team Files
compare to:
modelName
X
GWP 100a
Water
Impact
Price
Energy
Ecotoxicity
By Material
By Component
-
Aggregate
Top impact contributors
Prompts
Opportunity savings
Improvement metrics
-
-

## Slide 25: Next Steps
Automate merging of student CAD data with our Virtual Component Library & Database
Create visualisation app for decision making
Test with learners in the design module
Create a sustainable mechanism to maintain component library and database
Department of Engineering
francesco.ciriello@kcl.ac.uk
Dr Francesco Ciriello
Antoine El Adib
Department of Engineering
antoine.el-adib@kcl.ac.uk

## Slide 26: Example Case #1 : Plywood Material Sheet
Makersite plug-in works off of default Autodesk Fusion 360 material library

## Slide 27: Example Case #2 : Universal Joint (Huco)
Material cost is different from unit cost

## Slide 28: Example Case #3 : Li-Ion battery
No default material
cannot compute gCO2eq

## Slide 29: Example Case #4 : DC motor
Combination of copper, steel and plastic
Missing CAD models for internal components, e.g. armature
Probably incorrectly estimating mass as not hollow

## Slide 30: Example Case #5 : Fasteners e.g. McMaster Imports
reasonable estimates based on material

## Slide 31: Example Case #6 : Ship Assembly
Easy to identify foam as principal contributor to gCO2eq

## Slide 32
KING'S COLLEGE LONDON
SUSTAINABILITY EVALUATION OF OUR DESIGN MODULES
USING AUTODESK'S NEW FUSION 360
MAKERSITE ADD-ON

## Slide 33
King’s College London | Sustainable Design Modules
What’s
New?
01
Quality control update
04
Visualisers ideation
02
Chosen KPI investigation
05
Next steps
03
Integrating BOM & Database

## Slide 34
Item 1
Item 2
Item 3
Item 4
Item 5
50
40
30
20
10
0
Quality Control Results

## Slide 37
What do these numbers mean for us?
Quality increased however…
We noticed a jump in average performance per material from V1/V2,however, we are still far from achieving steady qualitative results.
Difference in gCO2eq values between M-S and our database increases with the number of manufacturing processes involved. If this is especially true for components in our targeted groups, it holds for other materials.
Makersite or Open-LCA?
Generally most of the errors came from uncertainties and unnecessary assumptions we could easily pinpoint and edit. However differences are still too important to be ignored.
Most of these errors might be linked to inappropriate manufacturing processes attribution in Open-LCA. It also is worth noting that we have very little information on how makersite performs calculations for us to address.
= we will perform a third round of quality control towards the end of the project

## Slide 38
Additional KPIs chosen
King’s College London | Sustainable Design Modules
Acidification potential - 100a (g202eq)
Acidification potential is crucial for engineers as it points directly to the product's effect on the environment's chemical balance. The release of sulfur dioxide equivalents can lead to acid rain and harm ecosystems. Understanding this metric helps us identify areas in our processes where we can minimize sulfur emissions and choose more environmentally friendly materials. It's an essential aspect of sustainable engineering design.

## Slide 39
King’s College London | Sustainable Design Modules
Ecotoxicity - multiple levels (g1,4DCBeq)
This KPI assesses the potential harm a product's lifecycle may inflict on ecosystems at multiple levels (human, terrestrial, aquatic...). It quantifies the release of toxic substances, often expressed in grams of 1,4-dichlorobenzene equivalents (g1,4DCBeq). High values of this KPI indicate a greater risk of contaminating ecosystems with harmful chemicals.
Water input (m3)
This KPI is important because it quantifies how much water our product consumes throughout its life cycle. By understanding our water consumption, engineers can develop strategies to minimize waste, recycle water, and choose production methods that are less water-intensive. This not only conserves resources but also reduces costs.

## Slide 40
King’s College London | Sustainable Design Modules
Energy input (MJ)
Oil and gas input (m3)
This KPI is intriguing because it highlights our product's reliance on these non-renewable resources. By closely examining this metric, engineers can explore alternative materials and energy sources, such as renewables and biofuels, to reduce our dependence on oil and gas. This shift not only makes our processes more sustainable but also helps us prepare for a future with dwindling fossil fuel reserves. NB: Oil amounts for total oil used throughout the product’s lifecycle.
This KPI represents the total energy required to produce and operate the product. It's fascinating because it reflects our product's energy efficiency and, consequently, its economic viability and environmental impact. By analyzing this data, engineers can optimize production processes, adopt energy-efficient technologies, and reduce our reliance on non-renewable energy sources.

## Slide 41
Connecting BOM to our database
Now that we have spent a considerable part of the project understanding LCA scopes and assessment methods and processes, we have collected significant data on our components and a range of KPIs.
But how we collect, store and communicate that data to students is crucial to completing their projects.
This is why before even thinking of sharing the data through visualisers we wanted to prototype through Python an early-stage product allowing our students to confront a BOM to our internal database automatically
King’s College London | Sustainable Design Modules

## Slide 42
Name | Material | Mass
Comp1 | A | 5
Comp2 | B | 2
Comp3 | C | 3
Name | Material | Class | KPIs
Comp4 | C | Comp | x
Comp5 | B | Comp | x
Comp1 | A | Stock | x
  Extract relevant data
Code runs through each row/component of the Makersite BOM
And checks for a match in our internal KPI Database
BOM Database
KPI Database

## Slide 43
Name | Material
Comp1 | A
Name | Material
Comp4 | C
Comp5 | B
Comp1 | A
Name | Material
Comp4 | B
2.Matchmaking: name and/or material
  1st row
  2nd row

## Slide 44
Comp 1 | A | KPI_1 | KPI_2 | ...
3.Preliminary storage in an empty dataframe

## Slide 45
Comp 1 | A | KPI_1 | KPI_2 | ...
Name | Material | Mass
Comp1 | A | 5
Comp 4 | 0 | 0 | 0 | 0
4.Conditional calculation
  If the component is not a consumable (i.e acrylic, plywood…)
  if no match
  else: leave intact in preliminary storage
*
+

## Slide 46
10
12
14
16
3
2
1
0
Item 1
20%
Item 2
20%
Item 3
20%
Item 4
20%
Item 5
20%
VISUALISERS
Using Plotly

## Slide 47
  monitors KPI values for each part of the assembly
  confronts it to a scale (either set by academics or industry standard)
  at a glance information and data (ecoivent documentation)
  same visualiser can be used for either:
  all KPI confrontation per part
  input chart per part
  output chart per part

## Slide 48
  gradual colour increase makes it clear which components are most expensive
  can be sorted per type (i.e stock material first) and compared to total stock material allowance
  cost overrun graphically shown and indicated in at a glance panel

## Slide 49
Our next steps
King's College London | Sustainable design modules
Research in further depth the visualisers offered by plotly
Research how we can include and use meshes as visualisers
Test our prototype through a range of BOMs and databases
Design 5+ visualisers to prototype the following weeks
Pinpoint the weaknesses of the program and harvest the structure of the BOM
Research and investigate how to extrcat and use hierarchy
RESEARCH
DESIGN&TEST